## Slide 1: EE 4130 – Systems Engineering “QFD/HOQ” Process
February 5, 2018
Prof. Joel Harris
CSULA - ECST Department

## Slide 2: Identifying Technical Performance Measures (TPMs)
Are quantitative values that describe system performance
They stem from system operational requirements…
They are Design Dependent Parameters (DDPs)
Examples:
  MTBF, MTTR, MDT, MTBM, etc.
They can also can include: weight, envelope, and availability to perform/function as designed

## Slide 3: Quality Function Deployment (QFD)
A somewhat dated, but nonetheless useful, method to identify and capture prime desires of the customer/consumer.
Employs cross-referenced matrices to perform comparisons of technical and design features, resulting in weighted values for TPMs.
Also compares competitive design parameters to proposed design for qualitative evaluation…

## Slide 4: Quality Function Deployment
Goal: To identify customer wants
Predict how the good/service/process will satisfy customer wants
Relates customer “wants” to system “hows”
Develops importance ratings/values
Evaluates competing products
Compares performance to desirable technical attributes (TPMs)

## Slide 5: Placement of QFD in System Development/Design Cycle
Leads designers into the preliminary design phase of the system development cycle.
Paves the way for functional requirement development (FFBDs)
Allows for functional allocation by partitioning of major system elements.
Permits identification of h/w and s/w items that multiple functions, simplifying the overall system architecture

## Slide 6: “System Design Flow”
Follows the progression from an abstract notion, to a systemic form/function, and ultimately to a repeatable, producible system/product.
The 4 Stages of design synthesis:
  1) Conceptual design, 2) system design, 3) preliminary design, and 4) critical design (all with their associated reviews)
Design reviews provide a formal method of checking the proposed design, provide a common baseline for all project stakeholders, permits solving of any interface issues, creates a record of design decisions and their rationale, and leads to a greater probability of a mature design when production starts.
Reduces risk associated with production phase activity w/r/t meeting requirements.

## Slide 7: QFD “House of Quality”
Relationship
matrix
How to satisfy
customer wants
Interrelationships
Competitive assessment
Technical
evaluation
Target values
What the customer
wants
Customer importance ratings
Weighted rating
Notes: 1

## Slide 8: “House of Quality” Example
Your team has been charged with designing a new digital camera for Great Cameras, Inc.
The first action is to construct a “House of Quality”

## Slide 9: House of Quality Example (cont’d)
Customer
importance
rating
(Scale of 1-5, 5 = highest)
Lightweight 3
Easy to use 4
Reliable 5
Easy to hold steady 2
Color correction 1
What the customer wants
What the Customer
Wants
Relationship
Matrix
Technical
Attributes and
Evaluation
How to Satisfy
Customer Wants
Interrelationships
Analysis of
Competitors

## Slide 10: House of Quality Example (cont’d)
What the Customer
Wants
Relationship
Matrix
Technical
Attributes and
Evaluation
How to Satisfy
Customer Wants
Interrelationships
Analysis of
Competitors
Low power requirements
Aluminum components
Auto focus
Auto exposure
Paint pallet
Ergonomic design
How to Satisfy
Customer Wants

## Slide 11: House of Quality Example (cont’d)
What the Customer
Wants
Relationship
Matrix
Technical
Attributes and
Evaluation
How to Satisfy
Customer Wants
Interrelationships
Analysis of
Competitors
Lightweight 3
Easy to use 4
Reliable 5
Easy to hold steady 2
Color corrections 1
High relationship (= 5)
Medium relationship (= 3)
Low relationship (= 1)
“Relationship matrix”

## Slide 12
What the Customer
Wants
Relationship
Matrix
Technical
Attributes and
Evaluation
How to Satisfy
Customer Wants
Interrelationships
Analysis of
Competitors
Relationships between the things we can do
Low power requirements
Aluminum components
Auto focus
Auto exposure
Paint pallet
Ergonomic design
House of Quality Example (cont’d)

## Slide 13: House of Quality Example (cont’d)
Weighted ratings (importance rating x relationship value)
What the Customer
Wants
Relationship
Matrix
Technical
Attributes and
Evaluation
How to Satisfy
Customer Wants
Interrelationships
Analysis of
Competitors
Lightweight 3
Easy to use 4
Reliable 5
Easy to hold steady 2
Color corrections 1
Our weighted ratings () 22 9 27 27 32 25

## Slide 14: House of Quality Example (cont’d)
Company A
Company B
G P
G P
F G
G P
P P
Lightweight 3
Easy to use 4
Reliable 5
Easy to hold steady 2
Color corrections 1
Our importance ratings 22 5
How well do the competing products meet customer wants?
What the Customer
Wants
Relationship
Matrix
Technical
Attributes and
Evaluation
How to Satisfy
Customer Wants
Interrelationships
Analysis of
Competitors

## Slide 15: House of Quality Example (cont’d)
Target values
(Technical attributes)
[Technical evaluation]
Company A 0.7 60% yes 1 ok G
Company B 0.6 50% yes 2 ok F
Our design 0.5 75% yes 2 ok G
0.5 A (low power)
75% (Al components)
2’ to ∞ (auto focus)
2 circuits (redundancy)
Failure: 1 per 10,000 ()
Panel ranking (design)
What the Customer
Wants
Relationship
Matrix
Technical
Attributes and
Evaluation
How to Satisfy
Customer Wants
Interrelationships
Analysis of
Competitors

## Slide 16: House of Quality Example (cont’d)
Completed House of Quality
Lightweight 3
Easy to use 4
Reliable 5
Easy to hold steady 2
Color correction 1
Our importance ratings
Low electricity requirements
Aluminum components
Auto focus
Auto exposure
Paint pallet
Ergonomic design
Company A
Company B
G P
G P
F G
G P
P P
Target values
(Technical attributes)
Technical evaluation
Company A 0.7 60% yes 1 ok G
Company B 0.6 50% yes 2 ok F
Our company 0.5 75% yes 2 ok G
0.5 A
75%
2’ to ∞
2 circuits
Failure 1 per 10,000
Panel ranking
22 9 27 27 32 25